## Slide 1
Toy-bubble models
e-NRTL → bubble thermodynamics in water electrolysis
Mathematical framework for bubble_enrtl_toy.py
Nomenclature follows the Grok draft and standard electrolyte-thermodynamics literature.

## Slide 2
Four-layer pipeline
Overview
A
Symmetric-reference e-NRTL
→ G^ex(T, P, {N_i}), μ_i, a_w, γ_±
B
Butler surface-tension equation
→ γ(m) = σ(m)
C
Axisymmetric Young–Laplace shape
→ bubble profile, V_d, r_cl
D
VLE & nucleation in H₂ bubble
→ y_H2, P_bub, r*

## Slide 3
Thermodynamic definition of surface tension
Starting point · Grok p. 3
Goal of Layer B: realise this derivative without a Langmuir fit, by placing the same e-NRTL model on both sides of the liquid–gas interface (Butler equation).

## Slide 4
Nomenclature (part 1)
§0
Symbol | Meaning | Units
T, P | temperature, pressure | K, Pa
Nᵢ, nᵢ | amount (extensive, molar) of species i | mol
xᵢ | mole fraction of species i | –
m | salt molality (mol / kg water) | mol kg⁻¹
zᵢ | signed charge of ion i | –
ν₊, ν₋, ν | stoichiometric coefficients | –
I_x | ionic strength, mole-fraction basis | –
I_m | ionic strength, molality basis | mol kg⁻¹
Aφ | Debye–Hückel parameter (water, 298 K) ≈ 0.392 | –
ρ | PDH closest-approach parameter = 14.9 | –
α_ij | NRTL non-randomness factor (fixed = 0.2) | –
τ_ij | NRTL binary interaction parameter | –
G_ij = exp(–ατ) | NRTL local-composition factor | –

## Slide 5
Nomenclature (part 2)
§0
Symbol | Meaning | Units
G^ex | total excess Gibbs energy | J
μᵢ | chemical potential of species i | J mol⁻¹
aᵢ = xᵢ γᵢ | activity of species i | –
γ_± | mean ionic activity coefficient (molality basis) | –
a_w | water activity | –
φ | osmotic coefficient | –
γ = σ | surface tension | N m⁻¹
Aᵢ | partial molar surface area of species i | m² mol⁻¹
σᵢ⁰ | surface tension of (hypothetical) pure component i | N m⁻¹
k_H | Henry's constant (solubility form), c = k_H p | mol kg⁻¹ Pa⁻¹
k_s | Sechenov (salting-out) coefficient | L mol⁻¹
R_bub | bubble radius | m
θ_g | contact angle through the gas phase | rad
V_d, D_d | detachment volume, diameter | m³, m
r* | critical nucleation radius | m
S, S₀ | supersaturation (effective / reference) | –
Subscripts: c = cation, a = anion, w = water/solvent, s = lumped salt, B = bulk, S = surface phase, 0 = reference / pure-water value.

## Slide 6
Layer A — Symmetric-reference e-NRTL
§1
• Total molar Gibbs energy Gʲ = ideal + PDH + NRTL
• Long-range: Pitzer–Debye–Hückel (symmetric, mole-fraction)
• Short-range: local-composition NRTL (lumped-salt form)
• Chemical potentials from ∂G^ex/∂nᵢ (symmetric finite difference)
• Water activity a_w and osmotic coefficient φ
• Mean ionic activity coefficient γ_±(m) via Gibbs–Duhem

## Slide 7
§1.1 Total molar Gibbs energy of liquid phase j
Layer A
Modern symmetric convention (Chen / Song & Chen, Aspen-style):
Excess part decomposed into a long-range Pitzer–Debye–Hückel term and a short-range local-composition (NRTL) term.

## Slide 8
§1.2 Long-range Pitzer–Debye–Hückel term
Layer A
Symmetric reference on mole-fraction basis (Chen & Evans 1986; Song & Chen 2009):
• Recovers DH limiting law ln γ_± → –|z₊z₋| Aφ √I_m as m → 0
• Responsible for the initial droop of γ_± (Fig. 1)
• Carries the charge structure → KOH vs H₂SO₄ diverge already at low m (Fig. 6)

## Slide 9
§1.3 Short-range local-composition NRTL term
Layer A
Single strong electrolyte + solvent with lumped-salt symmetric form; X_s = x_c + x_a:
• G_{ij} = exp(–α τ_{ij}), α = 0.2
• Two parameters per salt: τ_{sw} (salt→solvent) and τ_{ws} (solvent→salt)
• Like-ion repulsion enforced by lumping ion pair → τ_{cc} = τ_{aa} = 0 by construction

## Slide 10
§1.3 Toy-level caveat on the lumped-salt form
Layer A
Why the lumped form suffices here
• Full Chen symmetric e-NRTL keeps cation & anion as separate interacting species, with charge-weighted effective mole fractions X_i = |z_i| x_i for ions.
• That gives slightly different short-range non-ideality for asymmetric salts (e.g. H₂SO₄).
• We adopt the lumped form because:
• (i) the PDH part already carries the dominant charge-asymmetry at low–moderate m.
• (ii) ion-pair parameters for single-solvent binaries are effectively indistinguishable in their observable consequences (γ_±, a_w, φ) — they would just recalibrate.

## Slide 11
§1.4 Chemical potentials and activity coefficients
Layer A
In the code these partials are computed by symmetric finite difference on the extensive G^ex (chemical_potentials in bubble_enrtl_toy.py). Sidesteps hand-derivation errors; stable well below 1 mol/kg.

## Slide 12
§1.5 Water activity and osmotic coefficient
Layer A
At molality m with n_w = 1000 / M_w mol water per kg:

## Slide 13
§1.6 Mean ionic activity coefficient via Gibbs–Duhem
Layer A
To avoid the unsymmetric-to-molality reference-state transformation, integrate the solvent activity:
• Gives γ_± on the standard molality basis (pure water at infinite dilution = reference)
• Integral evaluated with scipy.integrate.cumulative_trapezoid on a 40-point molality grid

## Slide 14
Layer B — Butler surface-tension equation
§2
For a flat liquid–gas interface in LTE with the bulk, the chemical potential of each species equals in the surface phase (S) and bulk (B). One Butler equation per species:

## Slide 15
§2.2 Butler equation — system solve
Layer B
• For binary water + lumped-salt: a 2×2 system in (σ, x_s^S)
• σ eliminated by equating the water and salt equations → one nonlinear equation in x_s^S
• Solved with scipy.optimize.brentq in butler_surface_tension
• Reference: Butler, Proc. R. Soc. A 135, 348 (1932)
§2.3 Activity coefficients at the surface
• Li & Lu family (Langmuir 17, 3532, 2001; Hu & Lee FPE 158, 1043, 1999) couple surface phase to its OWN e-NRTL at surface composition.
• TOY approximation: γ_i^S(x^S) = γ_i^B(x = x^S) — the same e-NRTL evaluated at the surface composition.
• Preserves the Butler structure and gets the trend right; full surface-phase recalibration is a later refinement.

## Slide 16
§2.4 Partial molar surface area
Layer B
Stefan–Guggenheim / Sprow–Prausnitz form:
V_i = partial molar volume. Numerical values used in the toy are tabulated in §5.2.

## Slide 17
Layer C — Axisymmetric Young–Laplace shape & detachment
§3
• Young–Laplace ODE in arc-length parameterisation (from the apex)
• Contact-angle boundary condition through the gas phase
• Fritz-type quasi-static detachment force balance
• Solve for detachment volume V_d(σ, θ_g) and diameter D_d

## Slide 18
§3.1 Young–Laplace ODE (sessile bubble)
Layer C
Bubble on horizontal solid at z = 0, apex at z = H, buoyancy lifting upward. Arc-length s parameterisation from the apex:
• z_d = H – z (depth below apex); b = apex radius of curvature (shooting parameter)
• β = (ρ_l – ρ_g) g / σ
• IC: r(0)=0, z_d(0)=0, φ(0)=0
• Near-apex seeding with spherical expansion r ≈ b sin(s/b), z_d ≈ b(1–cos(s/b)) to avoid the r=0 singularity

## Slide 19
§3.2 Contact-angle boundary condition
Layer C
Contact angle θ_g measured THROUGH the gas phase at the three-phase line. The contact line is reached when the tangent angle satisfies:
• Integration terminates on this event (event_phi in young_laplace_shape)
• Secondary event catches pinch-off (r → 0 again)

## Slide 20
§3.3 Fritz-type detachment force balance
Layer C
Quasi-static detachment: buoyancy lifting the bubble equals the vertical component of surface tension at the pinning line
(Fritz, Phys. Z. 36, 379, 1935)
• Rooted on the shooting parameter b; detachment_volume scans b over a multiple of the capillary length ℓ_c = √(σ / Δρ g)
• Brackets the sign change and refines with brentq
• Output: V_d(σ, θ_g) and D_d = (6 V_d / π)¹ᐟ³

## Slide 21
Layer D — VLE and nucleation
§4
• Effective Henry's constant with salting-out (Sechenov OR a_w form)
• Bubble composition: Raoult for water + Laplace for P
• Critical nucleation radius r*(m) from Young–Laplace balance

## Slide 22
§4.1 Effective Henry's constant (salting-out)
Layer D
Two standard options, both produce the same trend in the toy:
• Sechenov uses tabulated k_s values
• Water-activity form uses a_w from the same e-NRTL — no extra parameter beyond §1
• Either route shifts solubility of a neutral gas (H₂) through the non-ideal water

## Slide 23
§4.2 Bubble composition (H₂ + H₂O vapour)
Layer D
Raoult with activity for water + Laplace for total pressure:

## Slide 24
§4.3 Critical nucleation radius
Layer D
At fixed dissolved-H₂ corresponding to reference supersaturation S₀ in pure water, the effective local supersaturation in salty electrolyte is:
Young–Laplace critical radius:
The compound behaviour of σ(m) ↑ and S_eff(m) ↑ pulls r* down sharply as m rises (Fig. 5 right panel).

## Slide 25
§5.1 e-NRTL parameters
Parameters
Salt | z_c | z_a | ν_c | ν_a | τ_sw | τ_ws | α
KOH | +1 | −1 | 1 | 1 | 11.5 | −4.5 | 0.2
H₂SO₄ | +1 | −2 | 2 | 1 | 13.0 | −5.2 | 0.2
Values are representative — tuned only to give qualitatively correct γ_±(m) and a_w(m) shapes:
• DH droop at small m
• NRTL rebound at large m
Published Aspen-style parameters for KOH–H₂O (Thomsen & Rasmussen, Chem. Eng. Sci. 54, 1787, 1999) should replace these once quantitative fidelity is wanted.

## Slide 26
§5.2 Butler parameters
Parameters
Species | σᵢ⁰ (N/m) | Aᵢ (m² mol⁻¹) | Vᵢ (m³ mol⁻¹)
H₂O | 0.07197 | 6.30×10⁴ | 1.80×10⁻⁵
KOH | 0.170 | 8.40×10⁴ | 2.70×10⁻⁵
H₂SO₄ | 0.155 | 1.31×10⁵ | 5.30×10⁻⁵

## Slide 27
§5.3 Henry, salting-out, nucleation · §5.4 General
Parameters
Parameter | Value | Note
k_H⁰ (H₂, 25°C) | 7.8×10⁻⁹ mol kg⁻¹ Pa⁻¹ | Sander, Atmos. Chem. Phys. 15, 4399 (2015)
k_s (KOH) | 0.134 L mol⁻¹ | ≈ Sechenov coefficient for H₂
k_s (H₂SO₄) | 0.099 L mol⁻¹ | ≈ Sechenov coefficient for H₂
θ_g | 30° | hydrophobic cavity, Raman-setup-like
S₀ | 2.0 | reference supersaturation in pure water
§5.4 General conditions
Parameter | Value
T | 298.15 K
P_atm | 1.01325×10⁵ Pa
ρ_l (water, 25°C) | 997.05 kg m⁻³
ρ_g (H₂, 25°C, 1 bar) | 0.0899 kg m⁻³
p_sat(T), 25°C | 3169 Pa
These constants define the reference state used throughout the toy. T and P_atm fix the e-NRTL and Butler evaluations; ρ_l, ρ_g feed the Young–Laplace shape (β = (ρ_l − ρ_g) g / σ) and the Fritz detachment balance; p_sat(T) sets the water partial pressure in the bubble (§4.2).

## Slide 28
§6 Salt vs. ions vs. electric field — what the toy captures
Discussion
Common confusion: “you're varying salt molality, not ion concentration or electric field — aren't those the bigger effects?” For a single, fully dissociated strong electrolyte these three are NOT independent.
• Ion concentration is set by salt molality via stoichiometry: c₊ = ν₊m, c₋ = ν₋m. KOH at 3 mol/kg means 3 mol/kg K⁺ AND 3 mol/kg OH⁻. Varying m IS varying ion concentration.
• Ionic strength: I_m = ½ Σ νᵢ zᵢ² m. For KOH, I_m = m; for H₂SO₄, I_m = 3m. PDH (§1.2) captures this exactly — that is why KOH and H₂SO₄ diverge in Fig. 1.
• Ion-identity effects beyond ionic strength come from the e-NRTL short-range τ parameters. Plotting σ vs I_m does NOT collapse the two salts onto one curve (Fig. 6 right panel) — specific-ion behaviour is real and captured by e-NRTL.

## Slide 29
§6 Electric-field / double-layer effects are NOT in this toy
Discussion
• They act at the ELECTRODE–electrolyte interface (polarised Pt), through:
• • Gouy–Chapman–Stern diffuse-layer structure
• • Lippmann equation, ∂σ/∂E = –q_s, linking electrode surface charge to electrocapillary depression
• • Frumkin correction to activation overpotential
• The bubble–electrolyte interface here is NOT polarised in the same way.
• It carries a weak ζ-potential (typically −30 to −50 mV for H₂ bubbles in water) from preferential ion adsorption — implicit in the Butler surface-phase composition.
A full treatment of electric-field effects on σ would add a Lippmann term:

## Slide 30
§7 Known limitations and extensions (1/2)
Limitations
# | Simplification | Path to improvement
1 | “Lumped-salt” NRTL (not full Chen-symmetric) | Full Chen 1986 / Aspen symmetric e-NRTL (two τ pairs per ion-solvent pair)
2 | Bulk e-NRTL used for surface activities in Butler | Couple a surface-phase e-NRTL as in Li & Lu 2001
3 | τ parameters chosen by trend, not fitted to data | Published Aspen parameters (Thomsen & Rasmussen 1999 KOH–H₂O; Clegg & Brimblecombe 1995 H₂SO₄–H₂O)
4 | Fritz-style vertical-force detachment | Pinch-off from the actual YL shape (watch r_neck → 0)
5 | Quasi-static bubble (no inertia / drag / Marangoni) | Couple σ(m) into dynamic integrators in ddgclib/dynamic_integrators/

## Slide 31
§7 Known limitations and extensions (2/2)
Limitations
# | Simplification | Path to improvement
6 | No double-layer / electrocapillarity | Add Lippmann correction to σ at polarised surface
7 | Sechenov form for salting-out | Derive salting-out directly from e-NRTL activity coefficient of dissolved H₂ (needs τ parameters for H₂–water and H₂–ion)
8 | Ideal-gas bubble (no H₂ fugacity correction) | Peng–Robinson or similar EoS for φ_H₂(T,P)
9 | Single solvent (water) | Extend to mixed solvents (water + methanol etc. for CO₂ electrolysis)
10 | Constant T, P | Add T, P dependence of all parameters (heavy but mechanical)

## Slide 32
§8 Primary literature the toy comments on
References
Sepahi et al. (2022) — the “Krug paper”
The effect of buoyancy-driven convection on the growth and dissolution of bubbles on electrodes. Electrochim. Acta 403, 139616. doi:10.1016/j.electacta.2021.139616
→ linear β, ideal gas, constant k_H, no composition-dependent σ
Raman et al. (2022) — the “Rivas paper”
Potential response of single successive constant-current-driven electrolytic hydrogen bubbles spatially separated from the electrode. Electrochim. Acta 425, 140691. doi:10.1016/j.electacta.2022.140691
→ fixed σ = 72 mN/m; concentration overpotential inferred by subtraction

## Slide 33
§8 Thermodynamic model foundations
References
Author | Reference | Topic
Butler, J. A. V. | Proc. R. Soc. A 135, 348 (1932) | Butler equation for surface tension
Chen, C.-C., Evans, L. B. | AIChE J. 32, 444 (1986) | symmetric e-NRTL (local composition, excess Gibbs energy)
Song, Y., Chen, C.-C. | Ind. Eng. Chem. Res. 48, 7788 (2009) | modern symmetric form
Li, Z.-B., Lu, B. C.-Y. | Langmuir 17, 3532 (2001) | Butler + e-NRTL coupling, aqueous electrolyte surface tensions
Hu, Y.-F., Lee, H. | Fluid Phase Equil. 158-160, 1043 (1999) | surface-phase formulation
Thomsen, K., Rasmussen, P. | Chem. Eng. Sci. 54, 1787 (1999) | published KOH–H₂O Aspen-style parameters
Fritz, W. | Phys. Z. 36, 379 (1935) | detachment force balance
Sechenov, I. M. | Z. Phys. Chem. 4, 117 (1889) | salting-out linear correlation
Sander, R. | Atmos. Chem. Phys. 15, 4399 (2015) | compilation of Henry's law constants (H₂, water)